## Slide 1: Arduino for Neuroscientists NBHVGR7040
AfN #1: Introduction, Simple Inputs and Outputs

## Slide 2
The World of Open Source Hardware and Software
Notes: What is open-source? A design philosophy, first and foremost. Currently, there are a wealth of open-source tools available of potential benefit to a neuroscientist.

## Slide 3: Uses of open-source hardware and software
3D printers / CNC
drones
Internet of things (IOT)
Interactive art

## Slide 4
Microcontrollers (MCUs)
Processors that run simple programs to control inputs and outputs.
Arduino (and arduino clones)
Parallax
Single-board computers
Linux-based (or Win) systems that run on ARM processors
Good for things that require more processing power, memory,
Raspberry Pi, Beaglebone black
Electronics
sensors, motors, amplifiers, etc.
Hardware:
Notes: Processing hardware such as microcontrollers and single-board computers allow a user to easily process and record diverse inputs derived from electronic circuits (e.g. sensors) and generate physical output. Electronic circuits act as sensory and motors systems, and the processing hardware acts as a central nervous system to let you change the logic of the sensory-motor transformation.

## Slide 5
Software:
Software for controlling the hardware
Arduino
Python
Software for online processing/analysis
(or complex stimulus pres.)
Python
Processing.org
R
Octave (~open MATLAB)
Notes: Open source software packages allow you to control hardware and record/process resulting data, and come with extensive communities of contributing users (if you ever have a problem, the odds are someone else has already encountered it, and solved it). Software defines the logic of the input-output transformation.

## Slide 6
Why Arduino?
Pros
Fast and consistent input/output (like spinal cord)
Easy to program (free software IDE and USB connec.)
Easily interfaces with analog and digital circuits (and computers)
Large community support
Cheap (~$30)
Cons
Single-threaded
Limited bandwidth
No true analog output
+5V/G only

## Slide 7: Arduino variants
larger
UNO
13 DIO
6 AD chan (8bit)
1 hard serial
Pro Mini
8 DIO
2 AD chan (8bit)
1 hard serial
No USB
(for embedded)
MEGA
54 DIO
10 AD chan (12bit)
4 hard serial
DUE
54 DIO
10 AD chan (12bit)
4 hard serial
DAC
3.3V
smaller

## Slide 8: A digital nervous system
Interactive digital systems as metaphor for the nervous system
a “hierarchical control system”
Arduino is like the spinal cord
Inputs and outputs: sensory and motor systems
Rapidly perform “behaviors” given particular inputs
PC
arduino
sensors
motors

## Slide 9: Arduino for Neuroscientists: Course objectives
Learn the features and limitations of the Arduino
Learn about a diverse toolbox of electronic sensors and motors.
Write Arduino programs to interact with these devices.
Interface the Arduino with a computer.
Combine these elements to design an interactive multimodal behavioral system.

## Slide 10: Course overview
AfN #1: Intro, Simple Inputs and Outputs
AfN #2: Advanced Input/Output
AfN #3: Motors, Data logging/computers
AfN #4: Advanced computer interface
AfN #5: Student projects
Notes: In this course, I want to give a practical, hands-on introduction to basic concepts and practice of Arduino programming and circuit design.

## Slide 11: AfN#1: Introduction, Simple Inputs and Outputs, Arduino shields
Anatomy of an Arduino
Input/Output overview
Your first Arduino program: Blink
  A simple Digital Output: digitalWrite(pin, STATE);
Digital Inputs
  Buttons/levers
  digitalRead(pin);
Analog Inputs
  Potentiometer input (voltage divider)
  analogRead(pin);
  Serial plotter
IR beam break detector
OpenMaze shields
TODAY:

## Slide 12
Anatomy of an Arduino
Digital input/outputs
Serial RX/TX (receive/transmit)
USB
(to computer)
Reset button
Analog inputs
+5V, GND
Ext. power
(if not from USB)
ATMEL
Microcontroller chip
An Arduino breaks out the most useful features of the ATMEL microcontroller chip into connectors (headers) that make it easy to interface with electronic circuits (e.g. sensors and motors), and program via USB.
Notes: Explain basic features of Arduino. Few things to point out: USB provides power (+5V), let’s you program the board via the IDE, and can be used to send serial output back to computer. Serial communication allows you to send information (e.g. words, numbers) back and forth from Arduino to computer, or other devices. Analog pins allow you to read electrical signals from sensors/circuits. Digital pins can be used as binary (HIGH/LOW = +5V/GND) inputs or outputs.

## Slide 13: Inputs and Outputs: Sensory and Motor Systems
Digital input/output
  digitalRead(readPin);
  digitalWrite(outPin, HIGH/LOW);
  TTL: 0/+5V
  Buttons: INPUT_PULLUP
  Digital communication protocols
    Using Arduino libraries
    Serial
    I2C, SPI
Analog input (and ~output)
  analogRead(readPin);
  8bit ADC
  analogWrite(PWM pin);

## Slide 14
Simple Digital Outputs:
Writing your first Arduino program, “Blink”
Initialize variables
Setup: define states of digital pins, set up other hardware (runs once)
Loop: runs over and over again, checking inputs and sending outputs (delays in ms)
1.) write program

## Slide 15
2.) select board and serial port
3.) upload to board
Notes: As an exercise, change the delays and see how it changes the pattern of flashing.

## Slide 16
Digital input (with a pushbutton switch)
Arduino Code
Breadboard:
Power/GND rails
Plug rows
Circuit
Notes: Discuss debouncing, floating inputs

## Slide 17: Analog input (with a potentiometer)
(TK: CODE)
Note: you don’t have to use pinMode on analog pins.

## Slide 18: Use serial plotter in the Arduino IDE to visualize potentiometer output via analogRead(A0);

## Slide 19
IR photogate/beam-break detector
X
Vout
(to A0)
IR LED
detector
Vout
Notes: Point out that when beam is unbroken, Q1 phototransistor resistance is low and Vout “hears” GND more than 5V, so voltage is LOW. When beam is broken, Q1 resistance is high and Vout “hears” 5V more, so voltage is HIGH. Use simple Serial.println(analogRead(0)); program and Tools>Serial Plotter to align LED (aligned when value is LOW/0 V ).

## Slide 20: Use serial plotter in the Arduino IDE to align LED and set threshold

## Slide 21
Write and upload program

## Slide 22
X
Vout (to A0)
IR LED
detector

## Slide 23: Arduino shields
Allow you to build dedicated circuits for interfacing with arduino

## Slide 24: OpenMaze Arduino shields a tool for design of automated behavioral tasks - cheap - flexible - easy to set up
pen
aze
openmaze.org
+
Behavioral system

## Slide 25
The OpenMaze website gives designs and instructions for interfacing with a variety of components useful in animal behavior experiments.
Hardware: 3D printing/laser cutting, PCB designs
Software: example code

## Slide 26: For this class: the OM2 board

## Slide 27: OM2 shield
Sol. Valve (12/5V, x4)
IR beam break detector (x4)
Hall effect sensor
Stepper/DC motor
MPR121 touch sensor (I2C, x12)
PGIO ports:
Speaker
Servo
Single touch
LED
Notes: Using this shield will allow us to try out a wide range of different devices without spending time on wiring.

## Slide 28: Problem Set #1:
Pavlovian conditioning
Printing times of nosepokes
Programming without using delay();
Using random(); , and creating exponential distributions.