## Slide 1: Arduino for Neuroscientists NBHVGR7040
AfN #2: More complex Inputs and Outputs

## Slide 2: Last time:
Simple Input/Output (“IO”)
  Digital output: Blink
    pinMode(pin, OUTPUT);
    digitalWrite(pin, HIGH/LOW);
    0V/+5V
  Digital input: button
    pinMode(pin, INPUT/INPUT_PULLUP);
    Val = digitalRead(pin);
    NOTE: debouncing
  Analog input: pot/IR
    0-5V > 0-1023
    No pin setup needed
    Val = analogRead(pin);

## Slide 3: This week:
More complex Input/Output (“IO”)
  “Debouncing” inputs
  Digital communication protocols
    Serial
    I2C/SPI
  Analog output
    Pulse-width modulation (PWM)
    analogWrite(pwmPin, freq.);
    tone(pin, freq., dur.);
  Digital output
    Getting around the 0/+5V limit
    Relays
    Transistors
    H-bridges
    Solenoid valves

## Slide 4: A few additional notes before we begin
Code:
  Integer types:
    int var=-32,768:32,767; (i.e. max ~33sec in millis, 2^16, 16bit)
    unsigned int var=0-65,535; (i.e. max ~66sec in millis)
    long var=-2,147,483,648:2,147,483,647; (max ~600hr, 32bit)
    unsigned long var=0-4,294,967,295; (max ~1200hr, 50days!)
Electronics:
  Ground everything together
  Then everything agrees on GND voltage
In setup(): randomSeed(floatingAnalogPin);

## Slide 5: “Debouncing” inputs
Simple thresholds may lead to spurious activations, due to sensor, environmental, or behavioral noise (voltage spikes, ambient light level changes, accidental animal contacts)
Thus “debouncing” in code sets a more stringent threshold, based upon the history of the input
Examples:
  Integrating signal over time
  Look for signal changes over local/recent baseline
Notes: Go through debounce example code to learn how to think through arduino flow logic

## Slide 6: Inputs and Outputs: sensory and motors systems
Inputs: analog and digital
Outputs: digital
  Primary limitation!: Arduino can only output 0/+5V
  PWM: to approximate analog output
  Working with larger and negative voltages
    Relays
    Transistors
    H-bridges
Digital communication protocols
  Serial
  I2C/SPI
Digital input/outputs
Serial RX/TX
Analog inputs

## Slide 7: Digital Communication protocols: Serial
Start in setup(), Serial.begin(baudRate);
RX=receive, TX=transmit
Buffered (i.e. can send/receive even when other stuff is going on)
But can have bottleneck (1ms/char?)
Send short messages

## Slide 8: Connecting arduinos with Serial
Connect multiple arduinos
Interface with some sensors (e.g. RFID)
MEGA/DUE have 4 hardware serial ports
Can use softwareSerial on other digital pins (but some limitations)

## Slide 9: Exercise: chit-chat with Serial
Find someone next to you, connect your TX with their RX and vice versa
Serial call-response
Parse incoming serial text, send output back depending upon input

## Slide 10: Talking to other chips: I2C and SPI
Talk to lots of digital sensor and control chips using same interface
Use same input pins (e.g. SDA:data, SCL:clock) to attach multiple devices
Uses device addressing
Control component behavior and get/set input/output (set registers)
Uses Wire library

## Slide 11: Connecting multiple devices with I2C
Many devices can use the same 2 wires (SDA,SCL) for I2C communication
Each must have a different address

## Slide 12: I2C commun. with MPR121 capacitive touch sensor
We will use this for our last exercise today to detect “mouse licks”…

## Slide 13: Analog Output (PWM, tone)
Analog output?
  PWM: pulse-width modulation
  analogWrite(pwmPin, dutyCycle0-255);
Approximating an analog signal with a digital output

## Slide 14: Fade
Use PWM with analogWrite(pwmPin, dutyCycle); to control the brightness of an LED
Plug LED into PWM (“~”) pin (e.g. pin 11)

## Slide 15: Tone
tone(pin, freq, dur); uses a built-in timer to deliver a sound on a digital pin (PWM not nec.)
“Non-blocking”: other things can take place during tone
NOTE: can interfere with other libraries that use the same timer (e.g. servo), especially on UNO.
Can also use tone to deliver pulse trains (e.g. for LEDs)
Arduino code:
buttonPullupTone_101817a.ino

## Slide 16: Digital outputs
Getting around the 0/+5V limitation
Relays
Transistors
H-bridges

## Slide 17: Relays
An electromechanical switch
Can carry DC or AC
Loud and relatively slow (compared to transistors)
Notes: Demo arduino relay extension cord

## Slide 18: Transistors
Basically a voltage-gated switch
Very fast (e.g. can PWM), and silent
Still can’t do negative Vs
NPN vs. PNP
Current gain β
50mA Arduino digital current may not be able to switch big current loads
Notes: For PNP, you ground the base to activate.

## Slide 19: Tricks for high current loads
For a normal BJT, beta = 50-200
Arduino digital outputs = 50mA
Thus Arduino can drive a transistor to saturation with 2.5-10A loads
Thus use Darlington pair or MOSFET (or “buckpuck” for LEDs)
MOSFET
Darlington pair
Buckpuck (~$15)

## Slide 20: Transistor arrays
ICs like the ULN2003/2803 array provide 7/8 darlington pair gates for a Vcc supply voltage.
Can therefore control many solenoid valves or a unipolar stepper motor.
But still can only carry current in one direction.

## Slide 21: H-bridges
H-bridges are transistor arrays that allow you to apply a larger supply voltage + or –
This makes it one of the single most useful components for controlling diverse devices

## Slide 22: OM2 shield
Sol. Valve (12/5V, x4)
Stepper/DC motor
Your OM2 board (named so because it has 2 H-bridges), has one H-bridge with 2-wire control for controlling one bipolar stepper, and one H-bridge that can independently control 4 solenoid valves, DC motors, etc.
Notes: Using this shield will allow us to try out a wide range of different devices without spending time on wiring.

## Slide 23: Solenoids (esp. solenoid valves)
Solenoid valves are useful for a variety of functions
  Liquid reward
  Airpuff punishment
  Olfactory stimuli

## Slide 24: Types of solenoid valves
Liquid or pneumatic (air)
2 way/ 3 way
5V (Lee)/12V/24V
Latching / non-latching
Pneumatic (Festo, SMI, Amazon)
Liquid (Parker, Lee Co.)

## Slide 25: Exercise: MPR121 touch sensing
Use Bildr code to read touch inputs with MPR121
MPR121 touch sensor (I2C, x12)

## Slide 26: Exercise: give water droplet upon touch input
Modify Bildr MPR121 code to open solenoid valves for a short time when touch port is activated.
MPR121 touch sensor (I2C)
Sol. valve
+12V