## Slide 1: Arduino for Neuroscientists NBHVGR7040
AfN #3: Motors, data logging, computer interface

## Slide 2: Last week:
More complex Input/Output (“IO”)
  “Debouncing” inputs
  Digital communication protocols
    Serial
    I2C/SPI
  Analog output
    Pulse-width modulation (PWM)
    analogWrite(pwmPin, freq.);
    tone(pin, freq., dur.);
  Digital output
    Getting around the 0/+5V limit
    Relays
    Transistors
    H-bridges
    Solenoid valves

## Slide 3: This week:
Motors
  DC motors
  Servos
  Stepper motors
Logging data
  SD card
Talking to computers
  Read serial with Python
  Record, parse, and plot

## Slide 4: DC motors
Single-coil motor
Use H-bridge to drive forward or backward
No position control
Goes at rate proportional to drive current

## Slide 5: Servo motors
Accurate (internal feedback circuitry)
Easy to control
Arduino Servo library
  PWM: 1pulse/20ms
  But watch out for timer conflicts
But slow and loud

## Slide 6: Different types of servos
Rotary and linear servos
Control is similar

## Slide 7: Stepper motors
Fast, quiet, and accurate
But more complex control circuitry (external)
Unipolar vs. bipolar
  Unipolar: easier to control, cheaper
  Bipolar: need H-bridge, but usu. higher-res. (200 steps/rev.)
Can lose steps if disengaged under asymmetric load

## Slide 8: Common stepper uses
Because of the speed, accuracy, quietness, and strength, they are used in a number of modern high-tech devices
3D printers, CNC mills
Microscope control

## Slide 9: Stepper control
Can use ULN2803 to control 2x unipolar
H-bridge for bipolar
Or use stepper driver (has current control, etc.)

## Slide 10: Bipolar steppers
Motor rotation dictated by stereotyped step sequence
Step sequence generated by Arduino Stepper library
Can use 4-wire or 2-wire control
Stepper drivers also allow microstepping, which can increase resolution

## Slide 11: Linear motion
Since most motors are inherently rotational, you need a mechanical apparatus to convert this into linear motion
Each primary motor type can drive linear motion
DC: linear potentiometer
Linear servo
Linear slide driven by stepper and XX drive

## Slide 12: Feedback/position sensing
With the exception of servo motors, which have internal position feedback circuitry, other types of motors need external circuitry to make sure they are in the right position
Some have internal potentiometers for position feedback
Limit switches can be used to reset position occasionally
  Mechanical
  Magnet / Hall effect sensor
Rotary encoders
  Quadrature encoding gives directional, high-res. Position feedback
  But can be too fast for Arduino if there are lots of other processes

## Slide 13: Motors Exercises
DC motor forward and backward with H-bridge
Servo with potentiometer
Stepper rotation

## Slide 14: Data logging
SD card (e.g. on Ethernet shield)
Computer
Ethernet/WiFi (UDP)

## Slide 15: SD card data logging
Can save serial text to text file on SD card
Can save tons of data without attached computer
Pop out card and analyze data on PC
Use SD shield (or one onboard Ethernet shield)

## Slide 16: Serial data logging (on a computer)

## Slide 17: Processing vs. Python: pros and cons
Both:
Free
Cross platform
Open Source
Large devel community
Diverse IO functionality
  Plotting
  Serial
  Multimedia
Easy to use, and get running
Syntax like Arduino (C)
Graphics oriented
Orig. for artists
Can use JAVA functions
Huge devel. community
Native on Linux
Can get MATLAB-like IDE (Spyder)
Can be tricky to get some things to work.
Notes: So Python has more overall functionality, largely due to an enormous development community, but it can be harder to get projects up and running.

## Slide 18: Spyder IDE (MATLAB-like envir. for Python)
Editor:
Like MATLAB, can run lines/blocks
Variable explorer:
Like MATLAB workspace
iPython console:
Like MATLAB command window

## Slide 19: Recording and plotting Arduino serial output with Python
serial
B
C
.txt file
Online plot (and PDF)
D

## Slide 20: Preview for next time: advanced computer interface
Webcam motion tracking and Arduino serial triggering
Visual operant tasks with PsychoPy and Arduino
Arduino behavioral apparatus workshop
A
B
C
Reward zone
1.
2.
3.